May 22, 2015

To:  Prospective Bidder

Subject:  Request for Proposals

Grand Valley State University is accepting proposals for one (1) Small Front-End Loader for our Grounds Department.  Reference attached bid information, instructions and specifications.

If you wish to bid on this equipment, please submit your proposals for bid #215-38 no later than 10:00 AM Tuesday, June 9, 2015. E-mail your proposal to: RFP-Received@gvsu.edu

Submit your proposal electronically to the above e-mail address by the bid opening date and time.  Grand Valley State University is not responsible for e-mail bids affected by spam or not received by the bid opening date & time.  No fax, verbal, or telephone proposals will be accepted.

Before submitting proposal, check to be sure that:

- The Proposal/Certification/Contract form is signed and witnessed.

- All addenda received are acknowledged

Note: Electronic submission becomes your authorized signature

Thank you for your participation,

Valerie Rhodes-Sorrelle, C.P.M.

Sr. Strategic Sourcing Specialist

Procurement Services – 2033 Zumberge Hall - Allendale, MI  49401

# Phone - 616/331-2283 - Fax 616/331-3287

### Grand Valley State University

### Bid Information & Instructions

Small Front-End Loader

Bid #215-38

- Grand Valley State University’s sales tax exempt no. 381684280

- Quote prices F.O.B. delivered to Allendale, MI - Pricing shall include all freight, set-up, installation, and dealer preparation.

- Reference attached Specifications

- Record all pricing information on the attached proposal & contract sheet in its entirety or the proposal may be rejected.

- Provide product availability

- All purpose, front end wheel loader must be new and a current production model.  Specifications are to be met to the best of the ability of the manufacturer and dealer, and any deviations from the attached specifications must be noted as an alternate.  Please send supporting documentation (pictures and written specifications) for any alternate front-end wheel loader submitted.  This will help us in our decision making process.

- GVSU is requesting a trade-in allowance for one (1) Bobcat Toolcat utility vehicle as part of your proposal.  Submit trade-in allowance as a separate line item on your proposal.

- Delivery to take place after July 1, 2015.  Payment of the invoice will not proceed until equipment has been delivered, inspected, and approved by the Grounds Supervisor, or an authorized/approved representative of GVSU.

- Unit must carry the manufacturer’s standard new machine warranty for a minimum twelve

(12) months.  A copy of the warranty must be attached to the bid proposal.  Any additional

available warranties may be described and priced as optional.

10.     Vendor/Dealer must supply one (1) copy of current product literature with proposal.

11.    Vendor/Dealer must supply one (1) current parts manual, and one (1) current service manual upon delivery of the front-end wheel loader.

12.   Grand Valley State University is requesting guaranteed pricing for at least 60 days after the bid opening date.

13.   Grand Valley State University endeavors to buy products made in the United States of America whenever an American-made* product is available that meets or exceeds the specifications requested and the price is equal to or lower than a foreign-made product.  Vendors are requested to bid American-made products and or services whenever available.  Vendors may bid foreign-made products or services when:

- They are specified

- They are identified as an alternate by the vendor as long as they are technically acceptable.

*More than 50% of the manufactured or assembled in the United States.

14.     At Grand Valley State University, socially responsible procurement -- which is defined as supporting diversity, socially responsible procurement, and sustainability -- is highly valued. These ideals are fundamental to our academic, research, and athletic excellence.  GVSU promotes supplier participation that is reflective of the diverse business community and of the University's desire to procure environmentally friendly products, while remaining focused on socially responsible procurement methodologies.

15.   GVSU reserves the right to accept or reject any or all Proposals not withdrawn before the opening date and to waive any irregularity or informality in the Proposal process.  The University reserves the right to conduct discussions, request additional information and accept revisions of Proposals from any or all bidders.  The University reserves the right to negotiate with the bidder whose proposal is deemed most favorable.

16.    Contact Valerie Rhodes-Sorrelle with any questions concerning this request for proposal at 616/331-2283

Small Front-End Loader

Specifications

Bid #215-38

ENGINE

- Wheel loader shall be equipped with a minimum four (4) cylinder, four (4) stroke, inline, high torque, low emission, oil/air or water cooled, fuel injected diesel engine,  developing not less than fifty four (54),  or exceed no more than sixty (60) net SAE horsepower.

- Engine shall meet all US EPA Tier 4i / Stage 3A emissions requirements for diesel engines.

- The unit will be equipped with a fuel filter, self-bleeding fuel system, and water separator.

- The unit will be equipped with a cold weather starting aid.

- The unit must be equipped with a two-stage air cleaner with service indicator lamp on the instrument panel.

- The unit shall be fitted with a full flow oil filter.

ELECTRICAL

- 1. Unit shall have a have a 12-volt system to include a battery with a      minimum 88Ah capacity,   and   an 80-amp alternator.

- The lighting system will include (2) front headlights w/low, (2) front work lights, and (2) rear work   lights, 92) rear stop/taillights, and turn signals with warning flashers.

- The machine will have a 12-volt outlet.

- The machine shall be equipped with a horn.

- The in cab instrumentations shall display the following machine conditions: engine temperature, engine oil pressure, hydraulic oil temperature, hydraulic oil filter, air filter restriction, parking brake, fuel level, travel (quick/slow), direction (forward/reverse), pre-heater, main light beam, direction indicators (left/right), battery charging, and differential locks.

- The unit shall be equipped with a neutral safety start.

- The battery shall be located outside of the cab, and in a lockable/secure location.

DRIVETRAIN

- Transmission shall be OEM designed and manufactured by the loader manufacturer and matched to the specific loader.

- The unit must have a fully hydrostatic drive with single lever shift control on the steering column for forward and reverse and high/low ranges.

- Single/inch brake pedal will be provided to control travel speed and max. engine rpm or direction is changed.

- The unit must be capable of attaining 12.0 mph in forward and reverse high range.

- The unit must have a filter installed in the suction line to protect the hydraulic system.

- The unit will be equipped with conventional differentials with 100% differential lock manually actuated by the operator inside the cab.

- The unit will have one single articulation/oscillation joint with rigid mounted front and rear axles.

- The transmission must have a mode selector enabling selection of a speed range to match specific applications.

STEERING

- The unit shall be equipped with an independent gear type pump feeding only the hydrostatic power steering.

- The steering cylinder will be double acting, and capable of articulation right or left.

Small Front-End Loader

Specifications Cont.

Bid #215-38

BRAKES

- Dead engine (hydrostatic) braking capability must be included.

- A parking brake capable of holding the unit on a slope will be included along with an instrument panel light and audible warning for parking brake engagement.

- The service brake system will be a friction type, externally mounted, centrally located and acting on all four wheels.

- Hydrostatic braking on all four wheels will be standard equipment.  Inch/brake pedal will reduce speed to 0 before the service brake is applied.

HYDRAULICS

- Independent gear type pump feeding only the hydraulic circuit will be provided.

- A three-spool control value will be provided as standard equipment.  Lift circuit to include raise, hold, and lower.  Tilt circuit to include rollback, hold, and dump.

- The unit shall be equipped with a common oil reservoir to supply work, steering, and drive hydraulics, and be filtered by a 10 micron filter on the oil return line.

- Hydraulic system reservoir must include a sight gauge for fluid level check.

- The system will be equipped with thermostatically controlled oil cooler for the work hydraulics and hydrostatics.

OPERATORS CAB

- The cab will meet SAE ROPS/FOPS safety standard with a lockable door that opens within the contour of the machine.

- The cab will be equipped with a heater/defroster effective on all windows.

- Other cab requirements are tilt steering wheel, cushioned/adjustable operator’s seat with retractable seat belt, emergency exit, front window must be tinted laminated glass, all other windows tinted safety glass, two speed windshield wiper with intermittent function, interior and exterior rear view mirrors, interior light, dashboard light, sun visor, and access steps and hand rails.

- Air conditioning must be available as an option from the loader manufacturer.

- Cab will have a lockable compartment for manuals.

- All instrumentation monitoring machine functions will be in full view of the operator.

- A diesel electric heater will be standard equipment.

- An audible backup alarm shall be included.

##### Grand Valley State University

Proposal & Contract

##### Bid #215-38

Contractor: ________________________________________________________________________________

Date: _________________________________________Bid No.: __________215-38_____________________

Project: Small Front-End Loader________________________________________________________________

Bid opening date and time: Tuesday, June 9, 2015 - 10:00 AM _______________________________________

Location: 2033 Zumberge Hall ______________________________________________________________

Allendale, MI, 49401_________________________________________________________________________

Attached or included are the following proposed Contract Documents:

- Introduction and Invitation to bid

- Instructions to Bidders

- Specifications

4.     Proposal & Contract

Bidder acknowledges receipt of the following addenda:

Addendum No. ____________ Dated ________________

Addendum No. ____________ Dated ________________

Documents listed herein, including all addenda issues pertaining to same, for the same, for the sum or sums stated below, and agrees that these documents will constitute the contract if accepted by Grand Valley State University.

The undersigned declares the following legal status in submitting this quotation:

[     ]	A corporation organized and existing under the laws of the State of ________________

[     ]	A partnership

[     ]	An individual doing business as (DBA) _______________________________________

The undersigned certifies that company is at least 51% owned, controlled and actively managed by:

( African American	            ( Asian American			( Hispanic American

( Native American    	            ( Woman/Women     	      		( Disabled Person(s)

( Veteran

The undersigned certifies that their company ____ IS or ____IS NOT currently debarred, suspended or proposed for debarment by any federal entity.  The undersigned agrees to notify the University of any change in this status, should one occur, until such time as an award has been made under this procurement action.

PROPOSAL SUM:  _____________________________________________dollars

One (1) Small Front-End Loader

($_______________________________)

Please provide unit cost for the following optional attachments. Attachments to be compatible with Small Front End Loader as specified in proposal:

(72) Inch snow blower with all mounting and hydraulics installed.

Cost:  _____________________________________________dollars

($_______________________________)

(10) Foot snow pusher box w/direct quick coupler mount.

Cost:  _____________________________________________dollars

($_______________________________)

(48) Inch pallet forks.

Cost:  _____________________________________________dollars

($_______________________________)

(0.5) to (1.5) cu. yd. material bucket.

Cost:  _____________________________________________dollars

($_______________________________)

Trade in Allowance: ____________________________________________dollars

One (1) Bobcat Toolcat Utility Vehicle

($_______________________________)

Pricing shall include all freight, set-up, installation, and dealer preparation.

Equipment bid on is “Green”          Yes ___   No ___ Environmentally Friendly        Yes ___     No ___

____________________________________________________________________________________

Company Name

____________________________________________________________________________________

Address                                                              		City/State/Zip Code

_________________________    _________________________    ______________________________

Telephone No.			   Fax No.                        	     E-Mail Address

___________________________________________    _______________________________________

Contractor's Signature                                                      Name & Title

___________________________________________    _______________________________________

Witness' Signature                                                            Name

___________________________________________     _______________________________________

Tax Identification No.                                                        Date

ACCEPTANCE:  This proposal is accepted by Grand Valley State University

__________________________________________    ________________________________________

Signature of Authorized Agent                                        Name & Title

_________________________    _________________________    ______________________________

Telephone No.			   Fax No.                        	     E-Mail Address

__________________________________________    ________________________________________

Witness' Signature                                                          Name

__________ 38 1684280______________________    ________________________________________

GVSU Tax Identification No.                                           Date

Proposals due Tuesday, June 9, 2015